## Slide 1: CS2100
Tutorial #5
MIPS Processor:
Datapath and control
(Prepared by: Aaron Tan)

## Slide 2
Generating ALUControl Signal
Opcode | ALUop | Instruction Operation | Funct field | ALU action | ALU control
lw |  | load word |  | add | 
sw |  | store word |  | add | 
beq |  | branch equal |  | subtract | 
R-type |  | add |  | add | 
R-type |  | subtract |  | subtract | 
R-type |  | AND |  | AND | 
R-type |  | OR |  | OR | 
R-type |  | set on less than |  | set on less than | 
ALUcontrol | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | slt
1100 | NOR
Generation of 2-bit ALUop signal will be discussed later
00
00
01
10
10
10
10
10
xxxxxx
xxxxxx
xxxxxx
10 0000
10 0010
10 0101
10 0100
10 1010
0010
0010
0110
0010
0110
0001
0000
0111
Instruction Type | ALUop
lw / sw | 00
beq | 01
R-type | 10
From lecture slide:
To tutors:
The first 3 slides are taken from the lectures. I will just tell students that these are the slides they should refer to while doing the questions in this tutorial. I am not going to explain these 3 slides.

## Slide 3
Design of ALU Control Unit (1/2)
Input: 6-bit Funct field and 2-bit ALUop
Output: 4-bit ALUcontrol
Find the simplified expressions
 | ALUop |  | Funct Field ( F[5:0] == Inst[5:0] ) |  |  |  |  |  | ALU control
 | MSB | LSB | F5 | F4 | F3 | F2 | F1 | F0 | 
lw |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  | 
sub |  |  |  |  |  |  |  |  | 
and |  |  |  |  |  |  |  |  | 
or |  |  |  |  |  |  |  |  | 
slt |  |  |  |  |  |  |  |  | 
0
0
X
X
X
X
X
X
0 0 1 0
0
0
X
X
X
X
X
X
0 0 1 0
0
1
X
X
X
X
X
X
0 1 1 0
X
1
0
1
0
0
0
0
0
0 0 1 0
1
0
1
0
0
0
1
0
0 1 1 0
1
0
1
0
0
1
0
0
0 0 0 0
1
0
1
0
0
1
0
1
0 0 0 1
1
0
1
0
1
0
1
0
0 1 1 1
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
ALUcontrol3 = 0
ALUcontrol2 = ?
ALUop0 + ALUop1 F1
From lecture slide:

## Slide 4
Control Design: Outputs
 | RegDst | ALUSrc | MemToReg | Reg Write | Mem Read | Mem Write | Branch | ALUop | 
 |  |  |  |  |  |  |  | op1 | op0
R-type |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
0
0
1
1
0
0
0
1
0
1
1
0
1
0
1
0
0
0
1
X
X
0
1
0
0
0
0
0
X
X
0
0
0
1
0
1
0
1
0
1
0
1
1
0
From lecture slide:

## Slide 5
0
1
0
1
0
1
1
0
lw $24, 0($15)
Q1(i)
100011 01111 11000 0000000000000000
R[rt] = M[R[rs]+SignExtImm]
Registers File |  |  |  | ALU |  | Data Memory | 
RR1 | RR2 | WR | WD | Opr1 | Opr2 | Address | Write Data
RegDest | 
RegWrite | 
ALUSrc | 
MemRead | 
MemWrite | 
MemToReg | 
Branch | 
ALUop | 
ALUcontrol | 
$15
$24
$24
0
MEM([$15]+0)
[$15]
0
[$15]+0
[$24]
1
1
1
0
1
0
00
0010
Next PC value = PC + 4
Red means the data is actually used.
Blue means the data is not used.
100011
01111
11000
00000 00000 000000
Opr1
Opr2
Easy, just copy from tables in previous slides.
1
1
0
0

## Slide 6
0
1
0
1
0
1
1
0
beq $1, $3, 12
Q1(ii)
000100 00001 00011 0000000000001100
If (R[rs]==R[rt]) PC=PC+4+BrAddr
Registers File |  |  |  | ALU |  | Data Memory | 
RR1 | RR2 | WR | WD | Opr1 | Opr2 | Address | Write Data
$1
$3
$3 or $0
[$1]-[$3] or MEM([$1]-[$3])
[$1]
[$3]
[$1] – [$3]
[$3]
Next PC value = PC + 4
or (PC+4) + (12×4)
000100
00001
00011
00000 00000 001100
Opr1
Opr2
RegDest | 
RegWrite | 
ALUSrc | 
MemRead | 
MemWrite | 
MemToReg | 
Branch | 
ALUop | 
ALUcontrol | 
X
0
0
0
0
X
1
01
0110
0
0
0
1
X
X

## Slide 7
0
1
0
1
0
1
1
0
sub $25, $20, $5
Q1(iii)
000000 10100 00101 11001 00000 100010
R[rd] = R[rs] – R[rt]
Registers File |  |  |  | ALU |  | Data Memory | 
RR1 | RR2 | WR | WD | Opr1 | Opr2 | Address | Write Data
$20
$5
$25
[$20] – [$5]
[$20]
[$5]
[$20] – [$5]
[$5]
Next PC value = PC + 4
000000
10100
00101
11001
00000
100010
Opr1
Opr2
RegDest | 
RegWrite | 
ALUSrc | 
MemRead | 
MemWrite | 
MemToReg | 
Branch | 
ALUop | 
ALUcontrol | 
1
1
0
0
0
0
0
10
0110
1
0
0
0

## Slide 8
0
1
0
1
0
1
1
0
Q2(a)
SUB instruction
Inst-Mem (400)
Reg.File (200)
Control (100)
MUX (ALUSrc)
(30)
ALU
(120)
MUX (MToR)
(30)
Reg.File
(200)
Not critical path
400+200+30+120+30+200 = 980ps
0
1
Inst-Mem
400ps
-------------
Adder
100ps
-------------
MUX
30ps
-------------
ALU
120ps
-------------
Reg-File
200ps
-------------
Data-Mem
350ps
-------------
Control/ALUControl
100ps
-------------
Lshft/signext/AND
20ps

## Slide 9
0
1
0
1
0
1
1
0
Q2(b)
LW instruction
Inst-Mem (400)
Reg.File (200)
Control (100)
ALU
(120)
MUX (MToR)
(30)
Reg.File
(200)
Not critical path
400+200+120+350+30+200 = 1300ps
Why is MUX (ALUSrc) not included this time?
DataMem
(350)
Inst-Mem
400ps
-------------
Adder
100ps
-------------
MUX
30ps
-------------
ALU
120ps
-------------
Reg-File
200ps
-------------
Data-Mem
350ps
-------------
Control/ALUControl
100ps
-------------
Lshft/signext/AND
20ps

## Slide 10
0
1
0
1
0
1
1
0
Q2(c)
BEQ instruction
Inst-Mem (400)
Reg.File (200)
Control (100)
ALU
(120)
AND
(20)
Not critical path
400+200+30+120+20+30 = 800ps
MUX (ALUSrc)
(30)
MUX (PCSrc)
(30)
How about the green path: PC  Adder  MUX (PCSrc)?
How about the purple path: Inst.Mem  SignExt  LeftShift  Adder  MUX(PCSrc)?
Inst-Mem
400ps
-------------
Adder
100ps
-------------
MUX
30ps
-------------
ALU
120ps
-------------
Reg-File
200ps
-------------
Data-Mem
350ps
-------------
Control/ALUControl
100ps
-------------
Lshft/signext/AND
20ps

## Slide 11
Q3(a)
Correct
Wrong!
add instruction
(i) One example where the incorrect processor still gives the right execution result.
(ii) One example where the incorrect processor gives the wrong execution result.
Many possible answers.
Make RT = RD.
Example: add $t0, $t1, $t0
Example: add $t0, $t1, $t2
$t2 instead of $t0 is picked as write register.
RegDst = 1
R[rd] = R[rs] + R[rt]
opcode
rs
rt
rd
shamt
funct

## Slide 12
Q3(b)
Correct
Wrong!
lw instruction
(i) One example where the incorrect processor still gives the right execution result.
(ii) One example where the incorrect processor gives the wrong execution result.
Make the first 5 bits of immediate value the same as the register number of RT.
Example: lw $a0, 8192($t0)
Anything other than (i).
RegDst = 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
$a0 = $4
8192 = 0x2000
R[rt] = M[R[rs] + SignExtImm]
opcode
rs
rt
immed

## Slide 13
Q3(b)
Correct
Wrong!
beq instruction
(i) One example where the incorrect processor still gives the right execution result.
(ii) One example where the incorrect processor gives the wrong execution result.
Anything will work, since error has no impact on branch instructions.
None.
RegDst = X

## Slide 14
Opr1
Opr2
0
1
0
1
1
0
0
1
Tutors: A spare diagram for your use.

## Slide 15
END OF FILE