## Slide 1: CS2100 Tutorial 4
Instruction Set Architecture
Slides by Theodore, adapted from Prof. Aaron’s slides

## Slide 2: Overview
Q1) Addressing modes
Q2) Instruction Set Architecture Styles
Q3) Counting instruction sizes in various ISAs
Q4) Number of instructions in an ISA

## Slide 3: Q1. Overview
Processor
100
$s0
160
$s1
200
$s2
240
$s3
300
$s4
10000
$t0
15000
$t1
20000
$t2
25000
$t3
30000
$t4
$s0 = 100 mem(100) = 1000
$s1 = 160 mem(160) = 1600
$s2 = 200 mem(200) = 2000
$s3 = 240 mem(240) = 2400
$s4 = 300 mem(300) = 3000
$t0 = 10000 mem(10000) = 100
$t1 = 15000 mem(15000) = 150
$t2 = 20000 mem(20000) = 200
$t3 = 25000 mem(25000) = 250
$t4 = 30000 mem(30000) = 300
Memory
100
1000
:
1600
:
2000
:
2400
96
Address
160
200
240
:
100
:
150
:
200
10000
15000
20000
:
:
Data
A word is 4 bytes in MIPS.

## Slide 4: Q1. Addressing modes
$s0 = 100 mem(100) = 1000
$s1 = 160 mem(160) = 1600
$s2 = 200 mem(200) = 2000
$s3 = 240 mem(240) = 2400
$s4 = 300 mem(300) = 3000
 | Operand | Target Memory Address | Content
(a) | $t1 $t2 | Not applicable Not applicable | 15000 20000
(b) | $s2 100($zero) |  | 
(c) | $t4 40($s2) |  | 
(d) | $s3 200($zero) |  | 
(e) | $t3 $zero($t1) |  | 
(f) | $s1 140($s1) |  | 
$t0 = 10000 mem(10000) = 100
$t1 = 15000 mem(15000) = 150
$t2 = 20000 mem(20000) = 200
$t3 = 25000 mem(25000) = 250
$t4 = 30000 mem(30000) = 300

## Slide 5: Q2. ISA Styles
Stack | Accumulator | Memory-Memory | Register-Register
push @src pop @dest add | load @src add @src store @dest | add @dest, @src1, @src2 | load $reg, @src add $dest, $src1, $src2 store $reg, @dest
push @a1 push @a2 add | load @a1 add @a2 | add @a0, @a1, @a2 | load $r1, @a1
a0 = a1 + a2;
a1 = a0 + a2;
a2 = a0 + a1;
Instruction set

## Slide 6: Q2. ISA Styles
Stack | Accumulator | Memory-Memory | Register-Register
push @src pop @dest add | load @src add @src store @dest | add @dest, @src1, @src2 | load $reg, @src add $dest, $src1, $src2 store $reg, @dest
push @a1 push @a2 add pop @a0 push @a0 push @a2 add pop @a1 push @a0 push @a1 add pop @a2 | load @a1 add @a2 store @a0 add @a2 store @a1 add @a0 store @a2 | add @a0, @a1, @a2 add @a1, @a0, @a2 add @a2, @a0, @a1 | load $r1, @a1 load $r2. @a2 add $r0, $r1, $r2 store $r0, @a0 add $r1, $r0, $r2 store $r1, @a1 add $r2, $r0, $r1 store $r2, @a2
a0 = a1 + a2;
a1 = a0 + a2;
a2 = a0 + a1;
Instruction set

## Slide 7: Q3. Counting instruction set sizes
Things to note:
  3 bits for opcode
  128 bytes of addressable memory
    Byte-addressing: we don't need to care about non-byte-aligned accesses
    7 bits needed (0-127) to represent each byte
  Fixed length instruction format
    Every instruction have the same length
  5 general-purpose registers
    3 bits needed to represent the registers
Stack
push @src
pop @dest
add
Accumulator
load @src
add @src
store @dest
Mem-Mem
add @d, @s1, @s2
Reg-Reg
load $reg, @src
add $d, $s1, $s2
store $reg, @dest

## Slide 8: Q3. Counting instruction set sizes
Note on word size:
  We use powers of two for word-size
  This makes life easy :D
Stack
push @src
pop @dest
add
Accumulator
load @src
add @src
store @dest
Mem-Mem
add @d, @s1, @s2
Reg-Reg
load $reg, @src
add $d, $s1, $s2
store $reg, @dest
 | #bits for longest instructions | #bytes for each instruction
Stack | 10 | 2
Accumulator | 10 | 2
Memory-Memory | 24 | 4
Register-Register | 13 | 2

## Slide 9: Q3b. Counting instruction set sizes
Stack | Accumulator | Memory-Memory | Register-Register
push @src pop @dest add | load @src add @src store @dest | add @dest, @src1, @src2 | load $reg, @src add $dest, $src1, $src2 store $reg, @dest
push @a1 push @a2 add pop @a0 push @a0 push @a2 add pop @a1 push @a0 push @a1 add pop @a2 | load @a1 add @a2 store @a0 add @a2 store @a1 add @a0 store @a2 | add @a0, @a1, @a2 add @a1, @a0, @a2 add @a2, @a0, @a1 | load $r1, @a1 load $r2. @a2 add $r0, $r1, $r2 store $r0, @a0 add $r1, $r0, $r2 store $r1, @a1 add $r2, $r0, $r1 store $r2, @a2
 | #bytes per instruction
Stack | 2
Acc. | 2
Memory-Memory | 4
Register-Register | 2

## Slide 10: Q4. Number of Instructions
An ISA has 16-bit instructions and 5-bit addresses; two classes of instructions: A has one address; B has two addresses.
Both classes exist, and encoding space is fully utilized.
Bonus:
What happens if we don't stipulate both classes existing?
What happens if we don't need the encoding space to be fully utilized?

## Slide 11: Q4. Number of Instructions
An ISA has 16-bit instructions and 5-bit addresses; two classes of instructions: A has one address; B has two addresses.
Both classes exist, and encoding space is fully utilized.
(a) What is the minimum total number of instructions?
Class A: ppppppppppp xxxxx
Class B: qqqqqq xxxxx yyyyy
11-bit opcode
address
6-bit opcode
address
address

## Slide 12: Q4. Number of Instructions
An ISA has 16-bit instructions and 5-bit addresses; two classes of instructions: A has one address; B has two addresses.
Both classes exist, and encoding space is fully utilized.
(a) What is the minimum total number of instructions?
Class A: ppppppppppp xxxxx
Class B: qqqqqq xxxxx yyyyy
11-bit opcode
address
6-bit opcode
address
address
Answer: 95

## Slide 13: Q4. Number of Instructions
An ISA has 16-bit instructions and 5-bit addresses; two classes of instructions: A has one address; B has two addresses.
Both classes exist, and encoding space is fully utilized.
(a) What is the maximum total number of instructions?
Class A: ppppppppppp xxxxx
Class B: qqqqqq xxxxx yyyyy
11-bit opcode
address
6-bit opcode
address
address

## Slide 14: Q4. Number of Instructions
An ISA has 16-bit instructions and 5-bit addresses; two classes of instructions: A has one address; B has two addresses.
Both classes exist, and encoding space is fully utilized.
(a) What is the maximum total number of instructions?
Class A: ppppppppppp xxxxx
Class B: qqqqqq xxxxx yyyyy
11-bit opcode
address
6-bit opcode
address
address
Answer: 2017

## Slide 15: End of Tutorial 4
Slides uploaded on github.com/theodoreleebrant/TA-2425S1
Email: theo@comp.nus.edu.sg
Anonymous feedback:
bit.ly/feedback-theodore
(or scan on the right)
(Also reminder for me to take attendance)