## Slide 1: CS2100 Tutorial 2
MIPS
Slides by Theodore, adapted from Prof. Aaron’s slides

## Slide 2: Overview
Q1) C to MIPS translation
Q2) MIPS instruction encoding
Q3) Completing MIPS code
Q4) MIPS Tracing

## Slide 3: Admin stuff
Discussion question:
  do on your own, discuss in Canvas, ask me if anything
MIPS Sheet
  take one (in-front), would be useful until exam time

## Slide 4: Prelude to Q1: C’s “short-circuit eval”
(If you took CS1101S, this should be familiar to you!)
Q: What’s the result of evaluating the following in C:
int main() {
if (1 > 2 && 5/0 > 3) {
print(“aye”);
} else {
print(“nay”);
}
}
Compile Error
Segmentation fault
“aye”
“nay”
None of the above

## Slide 5: Prelude to Q1: C’s “short-circuit eval”
(If you took CS1101S, this should be familiar to you!)
Q: If we switched the order of the operands…?
int main() {
if (5/0 > 3 && 1 > 2) {
print(“aye”);
} else {
print(“nay”);
}
}
Compile Error
Segmentation fault
“aye”
“nay”
None of the above

## Slide 6: Q1: C to MIPS
char str[size] = { ... }; // some string
int lo, hi, matched; // matched = 1 (palindrome);
// matched = 0 (not palindrome)
// Translate to MIPS from this point onwards
lo = 0;
hi = size-1;
matched = 1; // assume this is a palindrome
while ((lo < hi) && matched) {
if (str[lo] != str[hi])
matched = 0; // found a mismatch
else {
lo++;
hi--;
}}
Variable mappings:
lo  $s0;
hi  $s1;
matched  $s3;
Base address of str[]  $s4;
size  $s5

## Slide 7: Q1. C  MIPS
 | addi $s0, $zero, 0 | # lo = 0
 | addi $s1, $s5, -1 | # hi = size – 1
 | addi $s3, $zero, 1 | # matched = 1
loop: | slt $t0, $s0, $s1 | # (lo < hi)?
 | beq $t0, $zero, exit | # exit if (lo >= hi)
 | beq $s3, $zero, exit | # exit if (match == 0)
 | add $t1, $s4, $s0 | # addr of str[lo]
 | lb $t2, 0($t1) | # $t2 = str[lo]
 | add $t3, $s4, $s1 | # addr of str[hi]
 | lb $t4, 0($t3) | # $t4 = str[hi]
 | beq $t2, $t4, else | # compare str[lo], str[hi]
 | addi $s3, $zero, 0 | # matched = 0
 | j loop | # can also be “j endW”
else: | addi $s0, $s0, 1 | # lo++
 | addi $s1, $s1, -1 | # hi--
endW: | j loop | 
exit: |  | 
lo = 0; hi = size-1; matched = 1;
while ((lo < hi) && matched) {
if (str[lo] != str[hi]) matched = 0;
else { lo++; hi--;
}
}
Variable mappings: lo  $s0; hi  $s1; matched  $s3;
Base address of str[]  $s4; size  $s5

## Slide 8: Q1. C  MIPS
 | addi $s0, $zero, 0 | # lo = 0
 | addi $s1, $s5, -1 | # hi = size – 1
 | addi $s3, $zero, 1 | # matched = 1
loop: | slt $t0, $s0, $s1 | # (lo < hi)?
 | beq $t0, $zero, exit | # exit if (lo >= hi)
 | beq $s3, $zero, exit | # exit if (match == 0)
 | add $t1, $s4, $s0 | # addr of str[lo]
 | lb $t2, 0($t1) | # $t2 = str[lo]
 | add $t3, $s4, $s1 | # addr of str[hi]
 | lb $t4, 0($t3) | # $t4 = str[hi]
 | beq $t2, $t4, else | # compare str[lo], str[hi]
 | addi $s3, $zero, 0 | # matched = 0
 | j loop | # can also be “j endW”
else: | addi $s0, $s0, 1 | # lo++
 | addi $s1, $s1, -1 | # hi--
endW: | j loop | 
exit: |  | 
lo = 0; hi = size-1; matched = 1;
while ((lo < hi) && matched) {
if (str[lo] != str[hi]) matched = 0;
else { lo++; hi--; }
}
Variable mappings: lo  $s0; hi  $s1; matched  $s3;
Base address of str[]  $s4; size  $s5

## Slide 9: Q1. C  MIPS
 | addi $s0, $zero, 0 | # lo = 0
 | addi $s1, $s5, -1 | # hi = size – 1
 | addi $s3, $zero, 1 | # matched = 1
loop: | slt $t0, $s0, $s1 | # (lo < hi)?
 | beq $t0, $zero, exit | # exit if (lo >= hi)
 | beq $s3, $zero, exit | # exit if (match == 0)
 | add $t1, $s4, $s0 | # addr of str[lo]
 | lb $t2, 0($t1) | # $t2 = str[lo]
 | add $t3, $s4, $s1 | # addr of str[hi]
 | lb $t4, 0($t3) | # $t4 = str[hi]
 | beq $t2, $t4, else | # compare str[lo], str[hi]
 | addi $s3, $zero, 0 | # matched = 0
 | j loop | # can also be “j endW”
else: | addi $s0, $s0, 1 | # lo++
 | addi $s1, $s1, -1 | # hi--
endW: | j loop | 
exit: |  | 
lo = 0; hi = size-1; matched = 1;
while ((lo < hi) && matched) {
if (str[lo] != str[hi]) matched = 0;
else { lo++; hi--;
}
}
Variable mappings: lo  $s0; hi  $s1; matched  $s3;
Base address of str[]  $s4; size  $s5
Note 1: blt pseudo-instruction

## Slide 10: Q1. C  MIPS
 | addi $s0, $zero, 0 | # lo = 0
 | addi $s1, $s5, -1 | # hi = size – 1
 | addi $s3, $zero, 1 | # matched = 1
loop: | slt $t0, $s0, $s1 | # (lo < hi)?
 | beq $t0, $zero, exit | # exit if (lo >= hi)
 | beq $s3, $zero, exit | # exit if (match == 0)
 | add $t1, $s4, $s0 | # addr of str[lo]
 | lb $t2, 0($t1) | # $t2 = str[lo]
 | add $t3, $s4, $s1 | # addr of str[hi]
 | lb $t4, 0($t3) | # $t4 = str[hi]
 | beq $t2, $t4, else | # compare str[lo], str[hi]
 | addi $s3, $zero, 0 | # matched = 0
 | j loop | # can also be “j endW”
else: | addi $s0, $s0, 1 | # lo++
 | addi $s1, $s1, -1 | # hi--
endW: | j loop | 
exit: |  | 
lo = 0; hi = size-1; matched = 1;
while ((lo < hi) && matched) {
if (str[lo] != str[hi]) matched = 0;
else { lo++; hi--;
}
}
Variable mappings: lo  $s0; hi  $s1; matched  $s3;
Base address of str[]  $s4; size  $s5
Note 2: how to load

## Slide 11: Q1. C  MIPS
 | addi $s0, $zero, 0 | # lo = 0
 | addi $s1, $s5, -1 | # hi = size – 1
 | addi $s3, $zero, 1 | # matched = 1
loop: | slt $t0, $s0, $s1 | # (lo < hi)?
 | beq $t0, $zero, exit | # exit if (lo >= hi)
 | beq $s3, $zero, exit | # exit if (match == 0)
 | add $t1, $s4, $s0 | # addr of str[lo]
 | lb $t2, 0($t1) | # $t2 = str[lo]
 | add $t3, $s4, $s1 | # addr of str[hi]
 | lb $t4, 0($t3) | # $t4 = str[hi]
 | beq $t2, $t4, else | # compare str[lo], str[hi]
 | addi $s3, $zero, 0 | # matched = 0
 | j loop | # can also be “j endW”
else: | addi $s0, $s0, 1 | # lo++
 | addi $s1, $s1, -1 | # hi--
endW: | j loop | 
exit: |  | 
lo = 0; hi = size-1; matched = 1;
while ((lo < hi) && matched) {
if (str[lo] != str[hi]) matched = 0;
else { lo++; hi--;
}
}
Variable mappings: lo  $s0; hi  $s1; matched  $s3;
Base address of str[]  $s4; size  $s5
Note 3: lb vs lw

## Slide 12: Q1b.
 | addi $s0, $zero, 0 | 
 | addi $s1, $s5, -1 | 
 | addi $s3, $zero, 1 | 
loop: | slt $t0, $s0, $s1 | # (lo < hi)?
 | beq $t0, $zero, exit | # exit if (lo >= hi)
 | beq $s3, $zero, exit | # exit if (match == 0)
 | add $t1, $s4, $s0 | # addr of str[lo]
 | lb $t2, 0($t1) | # $t2 = str[lo]
 | add $t3, $s4, $s1 | # addr of str[hi]
 | lb $t4, 0($t3) | # $t4 = str[hi]
 | beq $t2, $t4, else | # compare str[lo], str[hi]
 | addi $s3, $zero, 0 | # matched = 0
 | j loop | # can also be “j endW”
else: | addi $s0, $s0, 1 | # lo++
 | addi $s1, $s1, -1 | # hi--
endW: | j loop | 
exit: |  | 
Variable mappings: lo  $s0; hi  $s1; matched  $s3;
Base address of str[]  $s4; size  $s5
add $t1, $s4, $s0 # addr. of str[lo]
add $t3, $s4, $s1 # addr. of str[hi]
slt $t0, $t1, $t3 # compare lo and hi addr
addi $t1, $t1, 1 # lo addr increment
addi $t3, $t3, -1 # hi addr decrement

## Slide 13: Prelude to Q2: MIPS Instruction Encoding
Remember and distinguish between R/I/J instructions!
  R-format instructions: operations using 3 registers OR shifts
    Example: add, and, slt, sll
  I-format instructions: operations using 2 register and an imm value
    Example: addi, beq, lw, sw
  J-format instruction: jump instructions
    Example: j, jal
  Other formats not in syllabus
    See reference data: there's FI/FR-formats for floats
    Assessments can have custom instruction formats!

## Slide 14: Prelude to Q2: MIPS Instruction Encoding
Be careful about the ordering!
Instruction:
add $t0, $t1, $t2
(opcode 0, funct 2016) rd (dest) rs (source) rt (target)
MIPS Reference Sheet:

## Slide 15: Q2: MIPS Instruction Encoding
addi $s1, $zero, 0

## Slide 16: Q2: MIPS Instruction Encoding
addi $s1, $zero, 0
rt = $s1 = $(16+1) = $17
rs = $zero = $0
rt rs SignExtImm

## Slide 17: Q2: MIPS Instruction Encoding
addi $s1, $zero, 0
rt = $s1 = $(16+1) = $17
rs = $zero = $0
rt rs SignExtImm

## Slide 18: Q2: MIPS Instruction Encoding
addi $s1, $zero, 0
rt = $s1 = $(16+1) = $17
rs = $zero = $0
rt rs SignExtImm
Ans:(2011 0000)16

## Slide 19: Q2: MIPS Instruction Encoding
0x11000002
=0b 0001 0001 0000 0000 0000 00000 0000 0010
First, check the opcode (first 6 bits), which is 0001002 = 416

## Slide 20: Q2: MIPS Instruction Encoding
0x11000002
=0b 0001 0001 0000 0000 0000 00000 0000 0010
Second, check the Reference Sheet for opcode 416.
Now we know it's a beq instruction with I-format.

## Slide 21: Q2: MIPS Instruction Encoding
0x11000002
=0b 0001 0001 0000 0000 0000 00000 0000 0010

## Slide 22: Q2: MIPS Instruction Encoding
0x11000002
=0b 0001 0001 0000 0000 0000 00000 0000 0010
opcode 000100 = 4
rs 01000 = 8
rt 00000 = 0
immediate 0100 = 2

## Slide 23: Q2: MIPS Instruction Encoding
0x11000002
=0b 0001 0001 0000 0000 0000 00000 0000 0010
opcode 000100 = 4
rs 01000 = 8
rt 00000 = 0
immediate 0100 = 2
$8 is $t0; $0 is $zero, and the immediate value is +2.

## Slide 24: Q2: MIPS Instruction Encoding
0x11000002
=0b 0001 0001 0000 0000 0000 00000 0000 0010
opcode --> beq
rs --> $t0
rt --> $zero
immediate --> +2

## Slide 25: Q2: MIPS Instruction Encoding
0x11000002
=0b 0001 0001 0000 0000 0000 00000 0000 0010
opcode --> beq
rs --> $t0
rt --> $zero
immediate --> +2
Ans: beq $t0, $zero, exit
 | MIPS code
 | addi $s1, $zero, 0
0x00084042 | Loop: srl $t0, $t0, 1
0x11000002 | 
0x22310001 | 
 | j loop
 | exit:
Next instr.
+2 instr.

## Slide 26: Q2: MIPS Instruction Encoding
0x22310001
=0b 0010 0010 0011 0001 0000 0000 0000 0001
opcode 0100002 = 816
This means addi instruction, I-format

## Slide 27: Q2: MIPS Instruction Encoding
0x22310001
=0b 0010 0010 0011 0001 0000 0000 0000 0001
opcode 0100002 = 816
This means addi instruction, I-format
0b 0010 0010 0011 0001 0000 0000 0000 0001
opcode rs rt imm (SignExtImm)

## Slide 28: Q2: MIPS Instruction Encoding
0x22310001
=0b 0010 0010 0011 0001 0000 0000 0000 0001
opcode 0100002 = 816
This means addi instruction, I-format
0b 0010 0010 0011 0001 0000 0000 0000 0001
opcode rs rt imm (SignExtImm)
816 1710 1710 110
$s1 $s1

## Slide 29: Q2: MIPS Instruction Encoding
0x22310001
=0b 0010 0010 0011 0001 0000 0000 0000 0001
opcode 0100002 = 816
This means addi instruction, I-format
0b 0010 0010 0011 0001 0000 0000 0000 0001
opcode rs rt imm (SignExtImm)
816 1710 1710 110
$s1 $s1
Answer: addi $s1, $s1, 1
inst rt rs imm

## Slide 30: Q2: MIPS Instruction Encoding
j loop
We first try to find the address of where we want to jump
0x00400028 + 4
= 0x0040002C
MIPS code | Address
addi $s1, $zero, 0 | 0x00400028
Loop: srl $t0, $t0, 1 | ?
j loop | 
exit: | 

## Slide 31: Q2: MIPS Instruction Encoding
j loop
We first try to find the address of where we want to jump
= 0x0040002C
= 0000 0000 0100 0000 0000 0000 0010 1100
As everything is word-aligned, we remove the last 2 bits;
To make it fit, we need to also throw away the first 4 bits.

## Slide 32: Q2: MIPS Instruction Encoding
j loop
We first try to find the address of where we want to jump
= 0x0040002C
= 0000 0000 0100 0000 0000 0000 0010 1100
As everything is word-aligned, we remove the last 2 bits;
To make it fit, we need to also throw away the first 4 bits.
Answer: 000010 000001000000000000000010
0000 1000 0001 0000 0000 0000 0000 1011
0 8 1 0 0 0 0 B

## Slide 33: Q2: MIPS Instruction Encoding
b) Give a simple mathematic expression for the relationship between $s1 and $t0
addi $s1, $zero, 0
loop: srl $t0, $t0, 1
beq $t0, $zero, exit
addi $s1, $s1, 1
j loop
exit:

## Slide 34
Q3(a)
Binary search
Variable
mappings:
addr. of
array[0]  $s0;
target  $s1;
lo  $s2;
hi  $s3;
mid  $s4;
ans  $s5.
MIPS code | Comment
loop: slt $t9, $s3, $s2 bne $t9, $zero, end | # while (lo <= hi) {
add $s4, $s2, $s3 [ ] | # mid = (lo + hi)/2
sll $t0, $s4, 2 add $t0, $s0, $t0 [ ] | # t0 = mid*4 # t0 = &array[mid] in bytes # t1 = array[mid]
slt $t9, $s1, $t1 beq $t9, $zero, bigger | # if (target < array[mid])
addi $s3, $s4, -1 j lpEnd | # hi = mid – 1
bigger:[ ] [ ] | # else if (target > array[mid])
addi $s2, $s4, 1 j lpEnd; | # lo = mid + 1
equal: add $s5, $s4, $zero [ ] | # else { ans = mid; break; }
lpEnd: [ ] | #} // end of while loop
end: | 

## Slide 35
Binary search
Variable
mappings:
addr. of
array[0]  $s0;
target  $s1;
lo  $s2;
hi  $s3;
mid  $s4;
ans  $s5.
MIPS code | Comment
loop: slt $t9, $s3, $s2 bne $t9, $zero, end | # while (lo <= hi) {
add $s4, $s2, $s3 [ ] | # mid = (lo + hi)/2
sll $t0, $s4, 2 add $t0, $s0, $t0 [ ] | # t0 = mid*4 # t0 = &array[mid] in bytes # t1 = array[mid]
slt $t9, $s1, $t1 beq $t9, $zero, bigger | # if (target < array[mid])
addi $s3, $s4, -1 j lpEnd | # hi = mid – 1
bigger:[ ] [ ] | # else if (target > array[mid])
addi $s2, $s4, 1 j lpEnd; | # lo = mid + 1
equal: add $s5, $s4, $zero [ ] | # else { ans = mid; break; }
lpEnd: [ ] | #} // end of while loop
end: | 
srl $s4, $s4, 1
lw $t1, 0($t0)
slt $t9, $t1, $s1
beq $t9, $zero, equal
j end
j loop
Q3(a)

## Slide 36
Q3.
MIPS code | Address
loop: slt $t9, $s3, $s2 bne $t9, $zero, end | 0xFFFFFF00
add $s4, $s2, $s3 srl $s4, $s4, 1 | 
sll $t0, $s4, 2 add $t0, $s0, $t0 lw $t1, 0($t0) | 
slt $t9, $s1, $t1 beq $t9, $zero, bigger | 
addi $s3, $s4, -1 j lpEnd | 
bigger: slt $t9, $t1, $s1 beq $t9, $zero, equal | 
addi $s2, $s4, 1 j lpEnd; | 
equal: add $s5, $s4, $zero j end | 
lpEnd: j loop | 
end: | 
(b) What is the immediate value in decimal for the “bne $t9, $zero, end” instruction?
end: is 16 instructions away from bne’s next instruction (add $s4, $2, $s3), so the immediate value is 16.
(c) If the first instruction is at address 0xFFFFFF00, what is the hexadecimal representation of this “j lpEnd”?
Address at lpEnd: is 0xFFFFFF00 + (1710×4) =0xFFFFFF44.
Removing the first 4 bits and last 2 bits, we put this into the immediate field. Opcode of j is 000010. Hence,
000010 1111 1111 1111 1111 1111 0100 01
= 0x0BFFFFD1
(d) Is the encoding of the second “j lpEnd” different from part (c)?
Same encoding. The two j instructions jump to the same address.

## Slide 37: End of Tutorial 3
Slides uploaded on github.com/theodoreleebrant/TA-2425S1
Email: theo@comp.nus.edu.sg
Anonymous feedback:
bit.ly/feedback-theodore
(or scan on the right)
(Also reminder for me to take attendance)