## Slide 1: CS2100 Tutorial 6
Boolean Algebra, Logic Gates & Simplification
Slides by Theodore, adapted from Prof. Aaron’s slides

## Slide 2: Recap
K-maps
minterm and Maxterm
Boolean Algebra laws

## Slide 3: Overview
Q1) Control values
Q2) Critical path / time calculation
Q3) Messing up inputs and hypotheticals

## Slide 4: Q1. Consensus theorem
x·y + x’·z + y·z = x·y + x’·z

## Slide 5: Q1. Consensus theorem
x·y + x’·z + y·z = x·y + x’·z
z
x
y
1
0
0
0
1
1
1
0

## Slide 6: Q1. Consensus theorem
x·y + x’·z + y·z = x·y + x’·z
z
x
y
1
0
0
0
1
1
1
0

## Slide 7: Q1. Consensus theorem
x·y + x’·z + y·z = x·y + x’·z
z
x
y
1
0
0
0
1
1
1
0
x·y + x’·z + y·z
= x·y + x’·z + 1·y·z [identity law]
= x·y + x’·z + (x+x’)·y·z [complement law]
= x·y + x’·z + x·y·z + x’·y·z [distributive law]
= x·y + x·y·z + x’·z + x’·y·z [commutative law]
= (x·y + x·y·z) + (x’·z + x’·y·z) [associative law]
= x·y + x’·z [absorption theorem 1]
Note: The dot is important!

## Slide 8: Q2a. Simplifying to SOP
F(x,y,z) = (x+yz’)(y’+y) + x’(yz’+y)
= (x+yz’)1 + x’(yz’+y) (by the complement law)
= (x+yz’) + x’(yz’+y) (by the identity law)
= x + yz’ + x’y (by absorption theorem 1)
= x + x’y + yz’ (by the commutative law)
= x + y + yz’ (by absorption theorem 2)
= x + y (by absorption theorem 1)

## Slide 9: Q2b. Simplifying to SOP
G(p,q,r,s) = ∏M(5, 9, 13)
5 = (0101)2; 9 = (1001)2; 13 = (1101)2

## Slide 10: Q2b. Simplifying to SOP
G(p,q,r,s) = ∏M(5, 9, 13)
= (p+q’+r+s’)  (p’+q+r+s’)  (p’+q’+r+s’) (by definition of maxterms)
5 = (0101)2; 9 = (1001)2; 13 = (1101)2

## Slide 11: Q2b. Simplifying to SOP
G(p,q,r,s) = ∏M(5, 9, 13)
= (p+q’+r+s’)  (p’+q+r+s’)  (p’+q’+r+s’) (by definition of maxterms)
(p+(q’+r+s’))  (p’+(q’+r+s’))
= (pp’) + (q’+r+s’)
Distributive law:
A + (BC) = (A+B)(A+C)
or (BC) + A = (B+A)(C+A)
= ((pp’) + (q’+r+s’))  (p’+q+r+s’) (by the distributive law)
5 = (0101)2; 9 = (1001)2; 13 = (1101)2

## Slide 12: Q2b. Simplifying to SOP
G(p,q,r,s) = ∏M(5, 9, 13)
= (p+q’+r+s’)  (p’+q+r+s’)  (p’+q’+r+s’) (by definition of maxterms)
= ((pp’) + (q’+r+s’))  (p’+q+r+s’) (by the distributive law)
= (0 + (q’+r+s’))  (p’+q+r+s’) (by the complement law)
= (q’+r+s’)  (p’+q+r+s’) (by the identity law)
= (q’(p’+q)) + (r+s’) (by the distributive law)
= p’q’ + r + s’ (by absorption 2)
Absorption theorem 2:
A  (A’+B) = AB
q’(p’+q) = q’(q+p’) = q’p’ = p’q’

## Slide 13: Q3. K-maps
m0
A
B
C
D
m1
m5
m4
m2
m3
m7
m6
m10
m11
m15
m14
m8
m9
m13
m12
m1: 0001 = A’B’C’D
m2: 0010 = A’B’CD’
m3: 0011 = A’B’CD

## Slide 14: Q3. K-maps
T(A,B,C,D) = Σm(0,1,2,4,5,9) + X(6,11,14,15).
T(A,B,C,D) = ∏M(3,7,8,10,12,13)  X(6,11,14,15).
(c)
A
B
C
D
m0
A
B
C
D
m1
m5
m4
m2
m3
m7
m6
m10
m11
m15
m14
m8
m9
m13
m12
(b)
(a)

## Slide 15: Q3. K-maps
T(A,B,C,D) = Σm(0,1,2,4,5,9) + X(6,11,14,15).
T(A,B,C,D) = ∏M(3,7,8,10,12,13)  X(6,11,14,15).
(c)
A
B
C
D
1
1
0
1
0
1
0
X
0
X
1
1
0
X
0
X
m0
A
B
C
D
m1
m5
m4
m2
m3
m7
m6
m10
m11
m15
m14
m8
m9
m13
m12
(b)
(a)

## Slide 16: Q3. K-maps
T(A,B,C,D) = Σm(0,1,2,4,5,9) + X(6,11,14,15).
T(A,B,C,D) = ∏M(3,7,8,10,12,13)  X(6,11,14,15).
m0
A
B
C
D
m1
m5
m4
m2
m3
m7
m6
m10
m11
m15
m14
m8
m9
m13
m12
(b)
(a)
(c)
A
B
C
D
1
1
0
1
0
1
0
X
0
X
1
1
0
X
0
X

## Slide 17: Q3. K-maps
(c)
A
B
C
D
1
1
0
1
0
1
0
X
0
X
1
1
0
X
0
X
(d)
How many PIs?
(e)
How many EPIs?

## Slide 18: Q3. K-maps
(c)
A
B
C
D
1
1
0
1
0
1
0
X
0
X
1
1
0
X
0
X
(f)
Simplified SOP expression:

## Slide 19: Q3. K-maps
(c)
A
B
C
D
1
1
0
1
0
1
0
X
0
X
1
1
0
X
0
X
(f)
Simplified SOP expression:
A'D'
+ A'C'
+ B'C'D
or
A'D' + A'C' + AB'D

## Slide 20: Q3. K-maps
(g)
K-map for T’:
(c)
A
B
C
D
1
1
0
1
0
1
0
X
0
X
1
1
0
X
0
X
K-map for T:
A
B
C
D

## Slide 21: Q3. K-maps
(g)
K-map for T’:
(c)
A
B
C
D
1
1
0
1
0
1
0
X
0
X
1
1
0
X
0
X
K-map for T:
A
B
C
D
0
0
1
0
1
0
1
X
1
X
0
0
1
X
1
X

## Slide 22: Q3. K-maps
(g)
K-map for T’:
(c)
A
B
C
D
1
1
0
1
0
1
0
X
0
X
1
1
0
X
0
X
K-map for T:
A
B
C
D
0
0
1
0
1
0
1
X
1
X
0
0
1
X
1
X

## Slide 23: Q3. K-maps
(g)
K-map for T’:
A
B
C
D
0
0
1
0
1
0
1
X
1
X
0
0
1
X
1
X
(g)
Simplified POS expression:
T’ =
T =

## Slide 24: Q3. K-maps
(g)
K-map for T’:
A
B
C
D
0
0
1
0
1
0
1
X
1
X
0
0
1
X
1
X
(g)
Simplified POS expression:
T’ = AD’ + CD + AB
T = (AD’ + CD + AB )’
= (A’+D)  (C’+D’)  (A’+B’)

## Slide 25: Q3. K-maps
T = A'D' + A'C' + B'C'D
2-level AND-OR circuit:
2-level NAND circuit:
T
A
B
C
D
A
B
C
D
T
Note: draw nicely :)
Rulers for lines
Thick dots for wire junctions
Unfilled circle on NAND gates

## Slide 26: Q4. Circuits with don’t-cares
K | L | M | N | X | Y | Z
0 | 0 | 0 | 0 |  |  | 
0 | 0 | 0 | 1 |  |  | 
0 | 0 | 1 | 0 |  |  | 
0 | 0 | 1 | 1 |  |  | 
0 | 1 | 0 | 0 |  |  | 
0 | 1 | 0 | 1 |  |  | 
0 | 1 | 1 | 0 |  |  | 
0 | 1 | 1 | 1 |  |  | 
K | L | M | N | X | Y | Z
1 | 0 | 0 | 0 |  |  | 
1 | 0 | 0 | 1 |  |  | 
1 | 0 | 1 | 0 |  |  | 
1 | 0 | 1 | 1 |  |  | 
1 | 1 | 0 | 0 |  |  | 
1 | 1 | 0 | 1 |  |  | 
1 | 1 | 1 | 0 |  |  | 
1 | 1 | 1 | 1 |  |  | 
X(K,L,M,N)
= 1 if KL = MN
or 0 otherwise
Y(K,L,M,N)
= 1 if KL  MN
or 0 otherwise
Z(K,L,M,N)
= 1 if KLM < LMN
or 0 otherwise
Assume input 0000 will not occur.
KL, MN are 2-bit unsigned integers.

## Slide 27: Q4. Circuits with don’t-cares
K | L | M | N | X | Y | Z
0 | 0 | 0 | 0 |  |  | 
0 | 0 | 0 | 1 |  |  | 
0 | 0 | 1 | 0 |  |  | 
0 | 0 | 1 | 1 |  |  | 
0 | 1 | 0 | 0 |  |  | 
0 | 1 | 0 | 1 |  |  | 
0 | 1 | 1 | 0 |  |  | 
0 | 1 | 1 | 1 |  |  | 
K | L | M | N | X | Y | Z
1 | 0 | 0 | 0 |  |  | 
1 | 0 | 0 | 1 |  |  | 
1 | 0 | 1 | 0 |  |  | 
1 | 0 | 1 | 1 |  |  | 
1 | 1 | 0 | 0 |  |  | 
1 | 1 | 0 | 1 |  |  | 
1 | 1 | 1 | 0 |  |  | 
1 | 1 | 1 | 1 |  |  | 
d
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
d
1
1
1
0
1
1
1
0
0
1
1
0
0
0
1
d
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
X(K,L,M,N)
= 1 if KL = MN
or 0 otherwise
Y(K,L,M,N)
= 1 if KL  MN
or 0 otherwise
Z(K,L,M,N)
= 1 if KLM < LMN
or 0 otherwise
Assume input 0000 will not occur.

## Slide 28: Q4. Circuits with don’t-cares
K | L | M | N | X | Y | Z
0 | 0 | 0 | 0 | d | d | d
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
K | L | M | N | X | Y | Z
1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
K
M
L
N
d
0
0
0
1
0
0
0
0
1
0
0
1
0
0
0
X
X = K'LM'N + KL'MN’ + KLMN
KLMN = 0000  X = 0

## Slide 29: Q4. Circuits with don’t-cares
K
M
L
N
d
1
1
0
1
1
0
0
1
1
1
0
1
1
0
0
Y
Y = MN + K'N + K'M + L'M
KLMN = 0000  Y = 0
K | L | M | N | X | Y | Z
0 | 0 | 0 | 0 | d | d | d
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
K | L | M | N | X | Y | Z
1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0

## Slide 30: Q4. Circuits with don’t-cares
K
M
L
N
d
1
1
0
0
1
0
0
0
0
1
1
1
1
0
0
Z
Z = K’
KLMN = 0000  Z = 1
K | L | M | N | X | Y | Z
0 | 0 | 0 | 0 | d | d | d
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
K | L | M | N | X | Y | Z
1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0

## Slide 31: End of Tutorial 6
Slides uploaded on github.com/theodoreleebrant/TA-2425S1
Email: theo@comp.nus.edu.sg
Anonymous feedback:
bit.ly/feedback-theodore
(or scan on the right)
(Also reminder for me to take attendance)