## Slide 1: CS2100 Tutorial 2
C and MIPS
Slides by Theodore, adapted from Prof. Aaron’s slides

## Slide 2: Overview
Q1) C bitwise operations
Q2) MIPS bitwise operations
Q3) MIPS Arithmetic
Q4) MIPS Tracing

## Slide 3: Q1: Bitwise Operations
Couple of bitwise operations that you should know:
bitwise OR |
bitwise AND &
bitwise XOR ^
bitwise NOT / 1s complement ~
left-shift <<
right-shift >>
In-class:
using a = 5 00000101
and b = 22 00010110
Note that left-shift also effectively multiplies by 2; the opposite for right-shift. Usually more efficient than normal multiplication!
Bonus: check out the difference between logical and arithmetic shift (not in syllabus)

## Slide 4: Q1: Ternary Operator
The conditional operator ? : is a shorthand to if-else
condition ? true-part : false-part
Equivalent examples:
if (a < 5) {
b = 10;
} else {
b = 15;
}
b = (a < 5) ? 10 : 15;

## Slide 5: Q2: MIPS Bitwise Operations
a. Set bits 2, 8, 9, 14, and 16 of b to 1. Leave all other bits unchanged.
Note: a register contains a 32-bit value, so b could look like this:
b = 00110000011100000110110100100001
and we want to change it to
b = 00110000011100010110111100100101
(Note: MSB is bit 31, on left, “upper” bits)

## Slide 6: Q2: MIPS Bitwise Operations
Step-by-step thought process:
Q: What do we need to change a bit to 1, regardless of the previous value?
A: Easiest way is to use OR; and OR the bit with 1
A | B | A OR B
1 | 1 | 1
0 | 1 | 1
1 | 0 | 1
0 | 0 | 0
Intermediate solution:
ori $s1, $s1, 0b00000000000000010100001100000100
Problem:
(Hint: see the immediate value / last operand)
Solution:
Load it up to a 32-bit register

## Slide 7: Q2: MIPS Bitwise Operations
Loading 0000 0000 0000 0001 0100 0011 0000 0100 into $t0:
Since we can only use 16 bits of imm value, we load the upper 16 bits with lui
lui $t0, 0b1
(Note: lui also clears the bottom 16 bits)
Then we load the bottom 16 bits using ori
ori $t0, $t0, 0b0100 0011 0000 0100
Finally we can call or between $s1 (b) and $t0
or $s1, $s1, $t0

## Slide 8: Q2: MIPS Bitwise Operations
b) Copy over bits 1, 3 and 7 of b into a, without changing any other bits of a.
Example, if initially:
a = … 1 0 0 0 1 1 1 1 0
b = … 1 1 1 1 1 0 0 1 0
We want the final result to be:
a = … 1 1 0 0 1 1 1 1 0

## Slide 9: Q2: MIPS Bitwise Operations
Step-by-step thought process:
Get bits 1, 3, 7 from b (say to $t0)
Get everything but bits 1, 3, 7 from a (say to $t1)
The result is $t0 OR $t1
Note: there are other ways to solve this question.
Exam question usually asks for the shortest possible answer, so any other 5-instruction correct answer gets full marks.
A | B | A AND B
0/1 | 1 | 0/1 (unchanged)
0/1 | 0 | 0
A | B | A OR B
0/1 | 0 | 0/1 (unchanged)
0/1 | 1 | 1

## Slide 10: Q2: MIPS Bitwise Operations
1. Get bits 1, 3, 7 from b/$s1 (say to $t0)
$s1 = … 1 1 1 1 1 0 0 1 0
mask = …
$t0 = … 0 1 0 0 0 0 0 1 0
A | B | A AND B
0/1 | 1 | 0/1 (unchanged)
0/1 | 0 | 0
A | B | A OR B
0/1 | 0 | 0/1 (unchanged)
0/1 | 1 | 1

## Slide 11: Q2: MIPS Bitwise Operations
1. Get bits 1, 3, 7 from b/$s1 (say to $t0)
$s1 = … 1 1 1 1 1 0 0 1 0
mask = … 0 1 0 0 0 1 0 1 0
$t0 = … 0 1 0 0 0 0 0 1 0
Answer:
andi $t0, $s1, 0b0000 0000 1000 1010
A | B | A AND B
0/1 | 1 | 0/1 (unchanged)
0/1 | 0 | 0
A | B | A OR B
0/1 | 0 | 0/1 (unchanged)
0/1 | 1 | 1
AND

## Slide 12: Q2: MIPS Bitwise Operations
2. Get everything but bits 1, 3, 7 from a/$s0 to $t1
$s1 = … 1 0 0 0 1 1 1 1 0
mask = …
$t1 = … 1 0 0 0 1 0 1 1 0
A | B | A AND B
0/1 | 1 | 0/1 (unchanged)
0/1 | 0 | 0
A | B | A OR B
0/1 | 0 | 0/1 (unchanged)
0/1 | 1 | 1

## Slide 13: Q2: MIPS Bitwise Operations
2. Get everything but bits 1, 3, 7 from a/$s0 to $t1
$s1 = … 1 0 0 0 1 1 1 1 0
mask = … 1 0 1 1 1 0 1 0 1
$t1 = … 1 0 0 0 1 0 1 0 0
Note that the mask has 1s all the way to the MSB – we get the same problem as Q2a; solution is the same (lui followed by ori)
Answer:
A | B | A AND B
0/1 | 1 | 0/1 (unchanged)
0/1 | 0 | 0
A | B | A OR B
0/1 | 0 | 0/1 (unchanged)
0/1 | 1 | 1
AND
lui $t1, 0b1111111111111111
ori $t1, $t1, 0b1111111101110101
and $s0, $s0, $t1

## Slide 14: Q2: MIPS Bitwise Operations
3. The result is $t0 OR $t1
Final answer:
A | B | A AND B
0/1 | 1 | 0/1 (unchanged)
0/1 | 0 | 0
A | B | A OR B
0/1 | 0 | 0/1 (unchanged)
0/1 | 1 | 1
andi $t0, $s1, 0b0000 0000 1000 1010
lui $t1, 0b1111111111111111
ori $t1, $t1, 0b1111111101110101
and $s0, $s0, $t1
or $s0, $s0, $t0

## Slide 15: Q2: MIPS Bitwise Operations
c) Make bits 2, 4, and 8 of c the inverse of bits 1, 3, and 7 of b
Thought process:
If we can isolate bits 1, 3, and 7 of b to $t0 and we move that into bits 2, 4, and 8, and we can invert it, this reduces to question 2b)
Note: “reduces to” means that we have converted a (usually harder) problem into another (usually solved) problem. You’ll see a lot of these in theoretical CS courses.

## Slide 16: Q2: MIPS Bitwise Operations
c) Make bits 2, 4, and 8 of c the inverse of bits 1, 3, and 7 of b
Step-by-step thought process:
Isolate bits 1, 3, and 7 of b/$s1 to $t0
Flip all bits
Shift one position left
Clear bits 2, 4, and 8 of c/$s2, and put in $t1
Answer is $t0 OR $t1
Note: Again, multiple valid answers. This slide does not give the same instructions as in the answer sheet as you will see later

## Slide 17: Q3. MIPS Arithmetic
c = a + b
add $sd2, $s0, $s1
Important: Note the “as few instructions as possible”
a  $s0 b  $s2
c  $s3 d  $s4

## Slide 18: Q3. MIPS Arithmetic
b) d = a + b – c
add $s3, $s0, $s1
sub $s3, $s3, $s2
Important: Note the “as few instructions as possible”
a  $s0 b  $s2
c  $s3 d  $s4
To think about: Why do we not need to zero $s3?
To think about: What operation(s) zeroes a register?

## Slide 19: Q3. MIPS Arithmetic
c) c = 2b + a – 2
add $s2, $s1, $s1 (alt: sll $s2, $1, 1)
addi $t0, $s0, -2
add $s2, $s2, $t0
Important: Note the “as few instructions as possible”
a  $s0 b  $s2
c  $s3 d  $s4
Bonus: Why does this not work?
srl $s2, $s0, 1 # c = a/2
add $s2, $s2, $s1 # c = a/2 + b
addi $s2, $s2, -1 # c = a/2 + b -1
sll $s2, $1, 1 # c = (a/2 + b – 1) * 2

## Slide 20: Q3. MIPS Arithmetic
d) 6a + 3 (b - 2c) = 3(2(a - c) + b)
sub $t0, $s0, $s2 # t0 = a – c
sll $t0, $t0, 1 # t0 = 2(a – c)
add $t0, $t0, $s1 # t0 = 2(a - c) + b
sll $t1, $t0, 2 # t1 = 4(2(a - c) + b)
sub $s3, $t1, $t0 # d = 3(2(a – c) + b)
Important: Note the “as few instructions as possible”
a  $s0 b  $s2
c  $s3 d  $s4

## Slide 21: Q4. MIPS Tracing
In-class tracing
add $t0, $s0, $zero
lui $t1, 0x8000
lp: beq $t0, $zero, e
andi $t2, $t0, 1
beq $t2, $zero, s
xor $s0, $s0, $t1
s: srl $t0, $t0, 1
j lp
e:

## Slide 22: End of Tutorial 2
Slides uploaded on github.com/theodoreleebrant/TA-2425S1
Email: theo@comp.nus.edu.sg
Anonymous feedback:
bit.ly/feedback-theodore
(or scan on the right)
(Also reminder for me to take attendance)